## Slide 1: Smart FOTA System
Shoubra Faculty of Engineering

## Slide 2: Team Members
Mazen Khaled
Abdelrahman
Ahmed Khaled
Yousif Anwar
Sayed Reda
FOTA Developer
Security Developer
V2V Developer
Problem Definition
Introduction to FOTA
Bootloader
01
02
03
Why cars need FOTA?
What is FOTA?
How flashing technique happens.
Working Flow
V2V Flashing
Security
PCB Design
04
05
06
How flashing V2V Works.
How we secure the over all system
Future Work
07

## Slide 3: Table of Contents
Problem Definition
Introduction to FOTA
Bootloader
V2V Flashing
Security
Future Work
01
02
03
04
05
07
Why cars need FOTA?
What is FOTA?
How flashing technique happens.
How flashing V2V Works.
How we secure the over all system
Working Flow
PCB Design
06

## Slide 4
01

## Slide 5
Working Flow

## Slide 6
Start
End
Divided To Groups
FOTA
V2V
Security
Project Integration
Error Happened?
Error Happened?
Error Happened?
No
No
No
Brainstorming To Solve the problems
Problem solved?
Gathering the Problems and ideas
Check with GP Mentor
No
Working Flow
Introduction
to FOTA
02

## Slide 7
02
Introduction
to FOTA
Integration of a reliable bootloader and a secure FOTA update mechanism ensures that devices can be updated remotely, enhancing their functionality, security, and reliability over time.
What is FOTA?

## Slide 8
Integration of a reliable bootloader and a secure FOTA update mechanism ensures that devices can be updated remotely, enhancing their functionality, security, and reliability over time.
What is FOTA?
Check for Update:
Determine the availability of newer firmware versions from the server (Firebase).
Get the Update from the Server:
This process encompasses establishing a secure connection, downloading the firmware update package, and validating the version of the downloaded update.
Encryption:
Implemented AES encryption as an advanced security measure, creating a unique code accessible only to your device and the server.
V2V:
Used to update the car via secure authenticated vehicles.
OTP For Authentication:
Used for verify the update to the user.
FOTA Features

## Slide 9
Developer
AES
Encryption
AES
Decryption
Vehicle 1
Vehicle 2
Firebase through https server
OTP Key
OTP Key
Car 1
Car 2
Processes Overview

## Slide 10
FOTA Features
Check for Update:
Determine the availability of newer firmware versions from the server (Firebase).
Get the Update from the Server:
This process encompasses establishing a secure connection, downloading the firmware update package, and validating the version of the downloaded update.
Encryption:
Implemented AES encryption as an advanced security measure, creating a unique code accessible only to your device and the server.
V2V:
Used to update the car via secure authenticated vehicles.
OTP For Authentication:
Used for verify the update to the user.

## Slide 11
Our Web-APP

## Slide 12
Our Web-APP

## Slide 13
Start
End
OEM Upload an encrypted update
OTP Entered?
Update car state on the server
Send OTP SMS Message with the update to the car owner Every 24h
No
Case 1
An update occurs through server.
Yes
Car Download file and decrypt it

## Slide 14
Start
End
Finding nearby authorized Vehicles V2
Car Received?
Updated vehicle 1
V1 Request an update
No
Case 2
An update occurs through V2V as car failed to connect to the server.
Send OTP SMS to V1 and V2 to prevent attacks
Car Received the file and decrypt it
Yes
03
Bootloader

## Slide 15
03
Bootloader
Updating…
What is a Bootloader?

## Slide 16
A bootloader is a small program that runs before the main application and facilitates firmware updates.
The bootloader’s primary role is to load and execute the application firmware.
What is a Bootloader?
Updating…
Developing a custom bootloader for STM32 MCU

## Slide 17
Developing a custom bootloader for STM32 MCU
Updating…
Normal way is to burn a code to an MCU is to use vendor application.
Vendor application required you with fixed communication protocol and with a specific bootloader architecture.

## Slide 18
Developing a custom bootloader for STM32 MCU
Host
Device
So, we built our Bootloader based on our application and the features we need.
Communication Protocol to flash is (UART).
Can Erase / Write on Flash memory.
Can Get the version of the current Bootloader.
Can Get Help with the Commands.

## Slide 19
Developing a custom bootloader for STM32 MCU

## Slide 20
Length | Command | Data | CRC
Address Write | NO Pages
(1 Byte) Length of Data.
(1 Bytes) For Determine Command.
Data with the commands (Pointer to an Address / page size) based on the command.
CRC (Cyclic Redundancy Check) Simple check sum error on (Length, Command, Data).

## Slide 21
Buffer which will be received by bootloader and send from Host
Length | Command | Data | CRC
(1 Byte) Length of Data.
(1 Bytes) For Determine Command.
Data with the commands (Pointer to an Address / page size) based on the command.
CRC (Cyclic Redundancy Check) Simple check sum error on (Length, Command, Data).
Address Write | NO Pages
Tx
Rx
Rx
Tx
Developing a custom bootloader for STM32 MCU

## Slide 22
Tx
Rx
Tx
Rx
04
V2V
Developing a custom bootloader for STM32 MCU

## Slide 23
04
V2V
ESP – NOW Protocol

## Slide 24
ESP – NOW Protocol

## Slide 25
Protocol developed by Espressif
Simple communications between ESP devices
Short packet transmission at 2.4 GHz
No WFI required, encrypted & unencrypted
ESP – NOW Protocol

## Slide 26
Unidirectional and Bidiectional modes
President connection after pairing
Works with ESP32 AND ESP8266
Long Range mode up to 480 meters
ESP – NOW Protocol

## Slide 27
One-way Communication
Initiator
Responder
ESP – NOW Protocol
Initiator
Initiator
Initiator

## Slide 28
Initiator
Responder
Initiator
Initiator
Initiator
One Responder, Multiple Initiator
ESP – NOW Protocol

## Slide 29
Two-way communication
ESP – NOW Protocol

## Slide 30
Two-way Network
ESP – NOW Protocol

## Slide 31
ESP – NOW Protocol
Mix & match ESP32 & ESP8266
Limit of 250 bytes per packet
Need Responders MAC Address

## Slide 32
MAC Address
C5
4C
F1
B2
67
AC
Media Access Control
6-digit hexadecimal number
Unique to every network device
ESP – NOW Protocol

## Slide 33
FF:FF:FF:FF:FF:FF is Broadcast MAC Address
ESP-NOW supports “pseudo-broadcast” mode
Broadcast to every device in the network
MAC Address
FF
FF
FF
FF
FF
FF
ESP – NOW Protocol

## Slide 34
Call back functions called during sending and receiving
Esp_now_register_rcv_cb(&function)
Called when data received
Returns received data
Esp_now_register_send_cb(&function)
Called when data sent
Returns sent state
Returns received status
ESP – NOW Protocol

## Slide 35
Send
Initialize ESP-NOW
Register a callback function upon sending
Add a peer device(receiver MAC address)
Send a message to the peer device
ESP – NOW Protocol

## Slide 36
Receive
Initialize ESP-NOW
Register a callback function upon receiving
Save message variable
ESP – NOW Protocol

## Slide 37
05
Security
System Architecture
What is the components we used in the V2V system?
V2V Integration with FOTA
How do we flash the code using v2v ?
Challenges faced use

## Slide 38
05
Security
Symmetric Encryption Algorithm
The Advanced Encryption Standard (AES)
Why AES ?
Security.
Performance.
Resource Efficiency.

## Slide 39
Symmetric Encryption Algorithm
The Advanced Encryption Standard (AES)
Why AES ?
Security.
Performance.
Resource Efficiency.
Problems
Unauthorized Access
Data Integrity Attacks
Man-in-the-Middle (MitM) Attacks

## Slide 40
Symmetric Encryption Algorithm
The Advanced Encryption Standard (AES)
Why AES ?
Security.
Performance.
Resource Efficiency.
Solutions
Encryption & Decryption (AES)
OTP

## Slide 41
Symmetric Encryption Algorithm
The Advanced Encryption Standard (AES)
Why AES ?
Security.
Performance.
Resource Efficiency.
To verify authorized user:
we used one-time password (OTP) For notify user with the new updates.
Why OTP ?
Security.
Authentication.
Convenience.

## Slide 42
To verify authorized user:
we used one-time password (OTP) For notify user with the new updates.
Why OTP ?
Security.
Authentication.
An Image from our OTP Sender
An Image from our OTP Receiver
An Image from our OTP Receiver

## Slide 43
An Image from our OTP Receiver
An Image from our OTP Sender
An Image from our OTP Receiver
06
PCB Design

## Slide 44
06
PCB Design

## Slide 45
07
Future Work

## Slide 46
07
Future Work

## Slide 47
Improved FOTA Update Mechanisms:
Delta Updates: Implement delta update mechanisms to transmit only software changes, reducing data usage and minimizing downtime.
Automatic OTP Serves:
Implement automatic One-Time Password services for enhanced security.
Future Work

## Slide 48
Artificial Intelligence and Machine Learning:
Predictive Maintenance: Integrate AI-driven systems to predict and address potential issues before they become critical.
Future Work

## Slide 49
Data Collection and Analysis:
Comprehensive Logging: Create detailed logs of all detected errors, including timestamps, vehicle IDs, locations, and environmental conditions.
Diagnostic Data: Collect diagnostic data from various vehicle systems to provide detailed information on errors' nature and causes.
Thank You
Abdulrhman Mohamed Abdelhamed
Ahmed Khaled Ahmed Zaky
Mazen Khaled Salah
Sayed Reda El Sayed
Yousef Mohamed Anwar

## Slide 50
Thank You
Abdulrhman Mohamed Abdelhamed
Ahmed Khaled Ahmed Zaky
Mazen Khaled Salah
Sayed Reda El Sayed
Yousef Mohamed Anwar